Semaine 2

---
Lecture
- Defect sizing in guided wave imaging structural health monitoring using convolutional neural networks (Roberto Miorelli, Clément Fisher, Andrii Kulakovskyi, Bastien Chapuis, Olivier Mesnil, Oscar D’Almeida, May 2021)
  - Trained a CNN on synthetic data
  - Location + size of defect
  - Delay and Sum algorithm
  - 1 emitter n-1 receivers

---
- On-plate autonomous exploration for an inspection robot using ultrasonic guided waves (Ayoub Ridani , Othmane-Latif Ouabi , Nico F. Declercq and Cédric Pradalier, Aug 2021)
  - Pulse s(t) is emitted
  - Response z(t) is received
  - Position known, only mapping
  - At each exploration step:
    - Frontier points are extracted from the grid map.
    - A utility function is used to evaluate the potential destinations.
    - The candidate pose with the highest utility is selected as the next goal.
    - The robot navigates to the target position.
  - Occupancy grid

---
Simulation